## Slide 1: Network Security
CSC 481/681/781
Principles of Computer Security
Reference: Goodrich and Tamassia, Chapter 5

## Slide 2: Networking Overview
Purpose: Allow computers and devices to talk to each other
Why:
  Sharing data: file servers, database servers, …
  Sharing devices: printers, CPUs (grid computing), ...
Since when?
  Internet dates back to ARPANET experiments in late 1960’s
  Phone line/modem connections from early 1960’s
  Ethernet from mid 1970’s
Changing dynamics:
  Past: Data over voice networks
  Now: Voice over data networks

## Slide 3: Types of Networks Classified by size/geographical area
Also (we won’t talk about this though):
PAN: Personal Area Network
  Coverage Range: 1–10 meters
  Key Technologies: Bluetooth, NFC, Infrared
  Real-World Example: Smartphone connected to wireless earbuds
  When It Is Used: For short-range communication between personal devices

## Slide 4: Types of Networks Classified by size/geographical area
LAN: Local Area Network
  Localized (room, building, cluster of buildings)
  High speed
  Key Technologies: Ethernet, Wi-Fi
  Real-World Example: Home or office Wi-Fi network
  When It Is Used: For fast and secure communication within a local location

## Slide 5: Types of Networks Classified by size/geographical area
Also (we won’t talk about this though):
CAN: Campus Area Network
  A CAN connects multiple LANs within a campus or a group of nearby buildings.
  Coverage Range: University or corporate campus
  Key Technologies: Ethernet, Fiber Optics
  Real-World Example: College or corporate campus network
  When It Is Used: To interconnect LANs across a campus under one organization

## Slide 6: Types of Networks Classified by size/geographical area
Also (we won’t talk about this though):
MAN: Metropolitan Area Network
  A MAN connects multiple networks within a city or metropolitan region.
  Coverage Range: City or large town
  Key Technologies: Fiber Optics, Microwave, Metro Ethernet
  Real-World Example: City-wide ISP network
  When It Is Used: To provide high-speed connectivity across a city

## Slide 7: Types of Networks Classified by size/geographical area
WAN: Wide Area Network (“Long haul network”)
  Widespread geographically, connects networks over large geographical areas such as countries – Lower speed
  Typically connections of multiple LANs
  Key Technologies: Leased lines, Satellite links, Internet
  Real-World Example: The Internet
  When It Is Used: To enable long-distance and global communication

## Slide 8: The Internet A collection of LANs
Basic idea: Network of networks
Internet (protocol) vs. “The Internet”
Switch/Hub

## Slide 9: The Internet A collection of LANs
Basic idea: Network of networks
Internet (protocol) vs. “The Internet”
Switch/Hub
Router

## Slide 10: Some Internet History
ARPA (Advanced Research Projects Agency) experiment to test ideas of “packet switched networks”
1969: First node goes on-line (UCLA)
1970’s: Maturing and apps (e-mail in 1972)
1980’s: Widespread in academic, military, and research communities
  1985: NSFNET
1990’s: The web and privatization

## Slide 11: The ARPANET in 1971

## Slide 12: Packet Switching A key concept from the ARPANET
Each packet sent independently
  Different pieces can be routed separately in a series of hops
    If MTU exceeded for hop, can break down further (fragments)
  Not dependent on a fixed “switched” connection, so can “re-route” easily to avoid trouble spots
Everything in the open, visible, and independent
  Good analogy: postcards
A B C D E F G H I J K L M N O P
A B C D
E F G H
I J K L
M N O P
Packet size determined by MTU (Maximum Transmission Unit)

## Slide 13: Network Layers OSI and Internet Models
OSI Model
What the user interacts with
Layer
7
6
5
4
3
2
1
Establishes a logical connection；
Ensures that data is delivered accurately；
Detects errors；
Controls the data transmission rate
Deals with MAC addresses and frames.

## Slide 14: Network Layers OSI and Internet Models
OSI Model
Layer
7
6
5
4
3
2
1
IP (or TCP/IP or Internet) Model
Application: HTTP, FTP, SMTP (E-mail)…
Transport: TCP, UDP
Network: IP (Internet Protocol)
Data Link + Physical

## Slide 15: Network Layers OSI and Internet Models
OSI Model
Layer
7
6
5
4
3
2
1
IP (or TCP/IP or Internet) Model
Application: HTTP, FTP, SMTP (E-mail)…
Transport: TCP, UDP
Network: IP (Internet Protocol)
Data Link + Physical
Next: We look at issues and vulnerabilities with each layer.

## Slide 16: First up: Physical and Link Layers

## Slide 17: Transmission Media Layers 1 and 2
How do the bits actually travel? (Physical Layer)
Wires
  LAN/Ethernet: Twisted pair or Coaxial cable
    Advantages: Very fast (Cat 5/5e/6 can do up to 1Gbps)
    Drawbacks: Signal attenuation limits high-speed distance
    Be careful about crosstalk, esp. in tight cable bundles!

## Slide 18: Transmission Media – Cont’d
Optical Fiber
  Light inside glass fibers instead of electrical signals
  Advantages:
    Very fast (10 Gbps or more)
    Less signal attenuation than copper
    Less interference and harder to tap (less signal leakage)
  Disadvantages:
    Interfaces not common for end-users
  Used mostly in backbones and long distance
    FDDI: Fiber-Distributed Data Interfaces
    Ethernet over fiber (up to 10 Gbps)
  Becoming more common to residential endpoints
    Verizon FiOS
    Google Fiber
    AT&T Fiber (AT&T U-verse)

## Slide 19: Transmission Media – Cont’d
Radio (Wireless)
  802.11a/b/g (WiFi) for LAN use
  Bluetooth – fast and cheap, but short range
  LTE and 802.16 (WiMax) – emerging for wide area
  Advantages: Convenience and reasonable speed
  Drawbacks: Broadcasting to the world!
    Encryption helps, but WEP is broken (WPA2 / 802.11i much better)
    Important to configure securely
    Jamming and signal blocking not difficult
  Security considerations: directional signals, spread spectrum, …
Microwave
  Line-of-sight transmission
    Limited by obstacles and curvature of earth
    But signals can be “bounced”

## Slide 20: Typical Building/Facility Ethernet
Fixed outlets wired to patch panel
  Located in “wiring closet” or server room
Patch panel to switch
Switch to router (higher layer issue!)

## Slide 21: Atypical Building/Facility Ethernet Unfortunately, maybe not as “atypical” as it should be...
Your wiring might not be on display, but…
… would you want to have to maintain either of these?
Neatness counts!

## Slide 22: Link Layer Ethernet

## Slide 23: Link Layer Ethernet
Has a "MAC table" that tracks which addresses are connected to which physical port

## Slide 24: Ethernet MAC Addresses
MAC = "Media Access Control"
Example MAC address: 00:1b:21:79:6b:52
Every network interface must have a unique address
(Common mistake: Thinking addresses are for computers, rather than interfaces)
How do manufacturers ensure addresses are unique?
00:1b:21
79:6b:52
:
Assigned to one manufacturer
Manufacturer chooses

## Slide 25: Manufacturer for given MAC prefix
First 24 bits of MAC address are assigned to a manufacturer
Several web sites will look up a MAC prefix and tell you the manufacturer
Example lookup using
http://hwaddress.com/
So MAC address in our previous example is from a network card manufactured by Intel.

## Slide 26: MAC Addresses Finding MAC address in Windows 11
"Physical Address" is MAC address

## Slide 27: Link Layer Threats and Vulnerabilities MAC Flooding Attack
When PC A sends a packet to PC B, PC C does not view packet sent between PC A and PC B
The attacker (in this instance PC C) floods the switch with packets, each with different source MAC address.

## Slide 28: Link Layer Threats and Vulnerabilities MAC Flooding Attack
If the memory where the MAC addresses are stored is full, the switch works like a hub

## Slide 29: Link Layer Threats and Vulnerabilities MAC Flooding Attack
There are three types of secure MAC addresses:
  Static secure MAC addresses
    Manually configured, stored in the address table, and added to the switch running configuration.
  Dynamic secure MAC addresses
    These are dynamically learned, stored only in the address table, and removed when the switch restarts.
  Sticky secure MAC addresses
    Dynamically learned or manually configured, stored in the address table, and added to the running configuration. If these addresses are saved in the configuration file, the interface does not need to dynamically relearn them when the switch restarts.

## Slide 30: Next: Network Layer

## Slide 31: Network Layer Overview
Purpose: Get data from one IP address to another
Machine-to-machine issues (no knowledge of applications)
Intermediate hops only look (usually!) at network layer
Exceptions:
“Traffic shaping”
Security monitoring
Proxies
  technically 2 connections

## Slide 32: Network Layer Issues IP Packets
Everything is “just bits” being transmitted
  Can all be tampered with!
  Header checksum is not cryptographic – for detecting transmission errors, not tampering
Common
Protocols
1 = ICMP
6 = TCP
17 = UDP
TTL = “Time to Live”
16 31
8 15
7
0
Data
Options (usually empty)
IP Destination Address
IP Source Address
Header Checksum
Protocol
TTL
Fragment Offset
Flags
ID (for fragmentation)
Total Length
ToS
IHL
Vers: 4

## Slide 33: Internet Addresses
IP = "Internet Protocol"
IPv4 addresses look like aaa.bbb.ccc.ddd
Each of the 4 numbers is in the range 0..255 (1 byte)
IPv6 addresses look like xxxx:xxxx:xxxx:... (all hexadecimal digits)

## Slide 34: Internet Addresses
Size of IPv4 addresses:
4 numbers, each one byte (8 bits)
Therefore, addresses are 32 bits
Why important? Means at most 232 different IP addresses.
232 is about 4 billion - what happens when we run out of IP addresses???
Oops - we are out of IP addresses!
Important points:
These addresses are "IPv4" (or IP version 4) addresses
With "IPv6" (version 6) - addresses are 128 bits
128 bits gives over 1038 addresses - we won't run out of these!

## Slide 35: Internet Addresses
IP address examples (simplified…):
All in UNCG SPAN Lab look like 152.13.218.???
General hosts in Petty Building look like 152.13.136.???
All on UNCG campus look like 152.13.???.???
All on North Carolina Research and Education Network like 152.?.?.?
So: All in the same LAN agree on the first three numbers
All on the same campus agree on the first two numbers
All in the same multi-campus network (NCREN here) agree on first number
Hierarchical addressing allows us to route messages between LANs
Note: This example is somewhat simplified (buildings, campuses, etc.). In reality things don't always match up to specific numbers in the IP address, but the ideas are similar!
More on how routing works next time… but first, what about local delivery?

## Slide 36: Local Delivery IP to Ethernet mapping using ARP
ARP = "Address Resolution Protocol"
Example:
152.13.136.18 wants to send "hello" to 152.13.136.25
Important points
Recognizes a "local connection" since only last number differs (technically: use netmask)
Problem: Local communication uses Ethernet MAC addresses

## Slide 37: Local Delivery IP to Ethernet mapping using ARP
MAC 00:1b:12:51:c3:ba
IP addr 152.13.136.18
MAC 03:2b:91:ac:52:9a
IP addr 152.13.136.21
MAC 00:1b:5a:31:14:a2
IP addr 152.13.136.25
MAC 00:33:9a:55:29:19
IP addr 152.13.136.33
Switch
ARP = "Address Resolution Protocol"
Example:
152.13.136.18 wants to send "hello" to 152.13.136.25
Important points
Recognizes a "local connection" since only last number differs (technically: use netmask)
Problem: Local communication uses Ethernet MAC addresses
To ff:ff:ff:ff:ff:ff (broadcast)
Who has 152.13.136.25?

## Slide 38: Local Delivery IP to Ethernet mapping using ARP
MAC 00:1b:12:51:c3:ba
IP addr 152.13.136.18
MAC 03:2b:91:ac:52:9a
IP addr 152.13.136.21
MAC 00:1b:5a:31:14:a2
IP addr 152.13.136.25
MAC 00:33:9a:55:29:19
IP addr 152.13.136.33
Switch
To: 00:1b:12:51:c3:ba
I have 152.13.136.25
at 00:1b:5a:31:14:a2
ARP = "Address Resolution Protocol"
Example:
152.13.136.18 wants to send "hello" to 152.13.136.25
Important points
Recognizes a "local connection" since only last number differs (technically: use netmask)
Problem: Local communication uses Ethernet MAC addresses

## Slide 39: Local Delivery IP to Ethernet mapping using ARP
MAC 00:1b:12:51:c3:ba
IP addr 152.13.136.18
MAC 03:2b:91:ac:52:9a
IP addr 152.13.136.21
MAC 00:1b:5a:31:14:a2
IP addr 152.13.136.25
MAC 00:33:9a:55:29:19
IP addr 152.13.136.33
Switch
To 00:1b:5a:31:14:a2
"hello"
ARP = "Address Resolution Protocol"
Example:
152.13.136.18 wants to send "hello" to 152.13.136.25
Important points
Recognizes a "local connection" since only last number differs (technically: use netmask)
Problem: Local communication uses Ethernet MAC addresses

## Slide 40: When ARP goes bad: ARP Spoofing
Performance: Hosts keep an “ARP Table” of known IP-to-MAC mappings
  Doesn’t have to ask if MAC address known
  Updates table with each “I have a.b.c.d” message
  Expires mappings regularly (in case IP moves)
In Windows: “arp –a”

## Slide 41: When ARP goes bad: ARP Spoofing
ARP spoofing: To sniff on a switched Ethernet
  Attacker (on same LAN) sends out “I have a.b.c.d” messages for target machine (or all machines!)
  Packets then sent to the attacker rather than the destination
  Attacker can then forward packets so no disruption – just monitoring

## Slide 42: ARP Spoofing Countermeasures
Static ARP tables
  Sensitive subnets should use static ARP tables
  Mappings don’t expire
  Mappings are hard-coded to be genuine by the administrator
  Not perfect: MAC address spoofing still possible!
Possible future directions:
  A better solution is still an unresolved research issue
  Some suggest authenticated ARP
    Uses digital signatures (PK Crypto), so slow – and ARP needs to be very low overhead!

## Slide 43: Subnet-to-subnet Communication Gateways and Routers
Router “lives on” multiple subnets
  Local address on each
  Can be more than 2 NICs / subnets
Routing tables say what goes where
  See with “/sbin/route” in Linux/Unix
  See with “route print” in Windows
129.12.61.1
72.1.19.53
Router
129.12.60.0/23
subnet
72.1.19.0/24
subnet
Destination Gateway Genmask Iface
129.12.60.0 0.0.0.0 255.255.254.0 eth0
0.0.0.0 129.12.61.1 0.0.0.0 eth0
Destination Gateway Genmask Iface
129.12.60.0 0.0.0.0 255.255.254.0 eth1
72.1.19.0 0.0.0.0 255.255.255.0 eth0
0.0.0.0 72.1.19.2 0.0.0.0 eth0
Sample simplified router routing table:
Sample simplified host routing table:

## Slide 44: Network Layer Attacks
Attack type 1: Put invalid data in fields
  Example 1: Ping of Death
    “Too large” ping packet crashes machine
  Example 2: LAND Attack
    Specially crafted packet with both source and destination set to victim address, with fields that make machine lock up
  Example 3: Jolt Attack (and Teardrop)
    Invalid fragmentation of packets that destination can’t reassemble, so machine freezes waiting for more
Attack type 2: Overwhelm network bandwidth
  Example: Ping flood
    Send rapid-fire “echo request” ICMP packets

## Slide 45: Network Layer Attacks Combining address spoofing with flooding
Smurf Attack (Simplified - just spoofing to hide attacker)
Attacker
24.3.29.123
Intermediary
123.45.67.89
Victim
209.12.17.35
Ping response to
Victim
Fake ping packet
with src 209.12.17.35
and dest 123.45.67.89

## Slide 46: Network Layer Attacks Combining address spoofing with flooding
Smurf Attack (DoS amplification)
Attacker
24.3.29.123
Victim
209.12.17.35
Fake ping packet
with src 209.12.17.35
and dest 123.45.67.255
Intermediaries
123.45.67.1
123.45.67.2
123.45.67.3
…
Many (up to 254) ping
responses to Victim

## Slide 47: Network Layer Attacks Combining address spoofing with flooding
Smurf Attack (DoS amplification)
Attacker
24.3.29.123
Victim
209.12.17.35
Fake ping packet
with src 209.12.17.35
and dest 123.45.67.255
Intermediaries
123.45.67.1
123.45.67.2
123.45.67.3
…
Many (up to 254) ping
responses to Victim
Works particularly well when Attacker-Intermediaries connection
is lower bandwidth than Intermediaries-Victim

## Slide 48: IP Spoofing Countermeasures
Filter out broadcast messages at gateway
  Doesn’t work if intermediary inside border!
  In general: Filter out LAN-only messages across border
Egress filtering
  Only let out packets with appropriate source addresses
  Doesn’t stop you from being an intermediary or a victim – think of it as “being a good netizen”